## Slide 1
SSA SUMMER TRAINING | JULY - AUGUST 2026
Noora AlQuaydhib Summer Training Summary
Scientific Gap Assessment and Payload Recommendation for RAMSES Mission for Asteroid (99942) Apophis
Supervised by Najla AlAhmadi & Rawan AlRayes

## Slide 2
Context
01
The Event
On 13 April 2029. Apophis passes within ~32,000 km from earth, closer than geostationary satellites, visible to the naked eye.
02
The RAMSES Mission
An international collaboration between ESA and JAXA. Currently under development and planned to launch in spring 2028, to arrive to Apophis in February 2029.
03
The Goal
An SSA instrument converts observer status into participant status on a joint ESA–JAXA mission.
1

## Slide 3
Study Objective & Scope
The second phase of a two-part study. The first selected the mission; this one determines the contribution.
WHERE THIS STUDY SITS
PHASE 1 — COMPLETED
Asteroid Mission Study
11 missions benchmarked → 2 prioritized → RAMSES selected.
PHASE 2 — THIS STUDY
Payload Study
What payload to put on the mission?
OBJECTIVE
Identify the knowledge gap where an additional payload would most increase the scientific return of RAMSES
SCOPE
2
The question is no longer whether to participate.
Phase 1 settled the mission. What remains is to put a specific technically credible contribution on the table while the build phase can still accommodate it.

## Slide 4
RAMSES Mission Overview
Rapid Apophis Mission for Space Safety , joint ESA–JAXA planetary defence mission.
TARGET & TIMELINE
Designation
Asteroid (99942) Apophis
Size
~375 m across
Taxonomy
Sq type, LL chondrite analogue
Launch
Spring 2028, H3 Rocket, Tanegashima
Arrival
February 2029
Close flyby
13 April 2029, ~32,000 km
O1
Shape, orbit and rotation
Before-and-after survey of shape, surface, orbit, rotation and orientation.
O2
Composition and interior
Composition, interior structure, cohesion, mass, density and porosity.
O3
Tidal response
How the asteroid responds to Earth's tidal forces.
O4
Solar System science
Insight into the formation and evolution of the Solar System.
Payload architecture: three platforms, twelve confirmed instruments
Main Orbiter
6 INSTRUMENTS
AFC (×2) · CHANCES · HAMLET · TIRI · RSE · RPS
Farinella: orbiter CubeSat
3 INSTRUMENTS
HORUS · Low-frequency radar · VISTA
Don Quijote: lander CubeSat
3 INSTRUMENTS
SIA · Gravimeter · MARIE
3
MISSION PUBLISHED OBJECTIVES

## Slide 5
Methodology
A structured analysis narrowed four knowledge gaps to one payload
RAMSES baseline
Studied the mission objectives, platforms and payloads
Mission Measurements
Broke the 4 mission objectives into 19 scientific measurements, mapped the 19 measurements into the 12 instruments of the mission
Knowledge gaps
Determined 4 knowledge gaps by identifying the non measured measurements and prioritized 1 knowledge gap
Payload trade study
Identified multiple instruments that can measure the knowledge gap
One recommended payload
4

## Slide 6
What RAMSES Already Measures
Confirmed payload by platform
Main Orbiter
AFC (×2)
Wide-field navigation imaging and shape mapping
CHANCES
High-resolution color imaging of surface change
HAMLET
Composition and space weathering, 650–1500 nm
TIRI
Surface temperature, thermal inertia, grain size
RSE
Radio tracking; gravity, spin state and tidal response
RPS
Ion and electron energy near the spacecraft
Farinella · Orbiter CubeSat
HORUS
Close-range imaging beyond orbiter resolution
Radar
Interior structure via dielectric sounding
VISTA
Volatile and organic content of captured dust
Don Quijote · Lander CubeSat
SIA
Seismic response to tidal stress and cracking
Gravimeter
Local density from gravitational acceleration
MARIE
Magnetic response during the Earth flyby
5
BASELINE KNOWLEDGE GAPS SELECTION RECOMMENDATION VALUE

## Slide 7
What the Mission Must Measure
The four objectives were decomposed into 19 measurements. Those 15 are already measured by the confirmed payloads
1
Read the objectives
ESA's four published aims, verbatim
2
Split into raw demands
one question per demand, no instrument named
3
Write the requirement
purpose, observable, threshold, boundary
4
Classify the type
direct, differential, or derived
O1
Shape, orbit and rotation
5 MEASUREMENTS
M1.1
Shape
M1.2
Surface
M1.3
Orbit
M1.4
Rotation
M1.5
Orientation
O2
Composition and interior
6 MEASUREMENTS
M2.1
Elemental composition
M2.2
Mineral composition
M2.3
Interior structure
M2.4
Cohesion
M2.5
Mass
M2.6
Density and porosity
O3
Tidal response
4 MEASUREMENTS
M3.1
Deformation
M3.2
Surface activity
M3.3
Spin-state change
M3.4
Deflection relevance
15/19 are measured. The four that are not are the knowledge gaps.
BASELINE KNOWLEDGE GAPS SELECTION RECOMMENDATION VALUE
6

## Slide 8
BASELINE KNOWLEDGE GAPS SELECTION RECOMMENDATION VALUE
Four Knowledge Gaps
Measurement openings the mission never set out to address, registered only where no confirmed instrument meets them.
GAP-1
Hydration state
GAP-2
GAP-3
Regolith grain-size distribution
GAP-4
Free Fe–Ni metallic phase fraction
7
Weathering-corrected composition
How much water and hydroxyl sit bound in the surface minerals: a record of whether water ever altered this body, and the basis of any volatile-resource case.
What the material is actually made of, beneath the thin rind that space alters. Every composition read from reflected light is biased until this is known.
How the loose surface material divides across particle sizes, from dust to boulders. It governs how regolith responds to disturbance and whether it can be processed.
How much of the iron is free Fe–Ni metal rather than bound inside silicates. Only the free fraction separates magnetically, so it carries the metal-resource case.

## Slide 9
1
Scientific value
Does the measurement return something scientifically unique and not predictable?
2
Mission compatibility
Can the orbiter already flying carry it, and does it add to the baseline rather than repeat it?
GAP-1
Hydration state
OUT · SCIENTIFIC VALUE
Apophis is an LL analogue, and LL chondrites are dry. The likely result is an upper limit, which confirms the taxonomy instead of testing it.
GAP-2
Weathering-corrected composition
CARRIED FORWARD
Nothing on board supplies an unweathered reference, the answer is not set by taxonomy, and the 2029 encounter may reset the maturity clock.
GAP-3
Regolith grain-size distribution
OUT · MISSION COMPATIBILITY
TIRI already maps grain size through thermal inertia. Measuring the distribution itself needs surface contact, which an orbiter payload cannot give.
GAP-4
Free Fe–Ni metallic phase fraction
OUT · SCIENTIFIC VALUE
LL is the lowest-metal ordinary chondrite class, so the answer is largely set in advance. The quantity is static too: any body, any year would serve.
BASELINE KNOWLEDGE GAPS SELECTION RECOMMENDATION VALUE
Priority Selection
Two criteria. A gap must clear both to be carried forward.
ONE PRIORITY
Weathering-corrected composition
8

## Slide 10
BASELINE KNOWLEDGE GAPS SELECTION RECOMMENDATION VALUE
The Scientific Problem
Space weathering changes what we see without changing the bulk composition.
Fresh material
Space weathering
Altered optical spectrum
Biased mineralogical interpretation
RAMSES can measure the spectrum,
BUT it cannot independently measure the reference needed to correct it.
The correction closes on itself
HAMLET's maturity map is derived from the spectrum it would correct, which makes it verifiable only against its source
Why it matters at Apophis
Sq type: a surface partly but not wholly refreshed. The 2029 encounter may reset the maturity clock, a natural experiment that will not recur.
9
Public عام

## Slide 11
BASELINE KNOWLEDGE GAPS SELECTION RECOMMENDATION VALUE
The Required Observable
What measurement would fill the gap?
Independent elemental abundance
of the near-surface regolith
1
From orbit
A specific reference from a single landing cannot travel across a body, so the measurement will be observed from the orbit.
2
Below the weathered surface
Sampling depth must exceed the altered layer, or the reference carries the bias it was meant to remove.
10
Public عام

## Slide 12
BASELINE KNOWLEDGE GAPS SELECTION RECOMMENDATION VALUE
Candidate Payload Assessment
Five candidate payloads were assessed against the required observable and the orbiter, only architecture.
Mössbauer Spectrometer
✕
Landing required
MicrOmega Microscope
✕
Landing required
LIBS, ChemCam class
✕
Close-range operation required
Neutron Spectrometer
!
Partial scientific match
Gamma-Ray Spectrometer
✓
Direct match
Full five-criteria assessment in appendix.
11
Public عام

## Slide 13
BASELINE KNOWLEDGE GAPS SELECTION RECOMMENDATION VALUE
Recommendation
RECOMMENDED PAYLOAD ENHANCEMENT
Gamma-Ray Spectrometer
RAMSES Main Orbiter
WHY
01
Independent of reflected light
02
Measures elemental abundance
03
Samples below the weathered layer
04
Strengthens HAMLET's interpretation
05
Fits the existing mission architecture
HAMLET
Mineralogy
+
GRS
Elements
12
More efficient
composition
Public عام

## Slide 14
BASELINE KNOWLEDGE GAPS SELECTION RECOMMENDATION VALUE
Implementation Route
A proven implementation route exists
APL
Johns Hopkins Applied Physics Laboratory
Instrument build & integration
LLNL
Lawrence Livermore National Laboratory
High-purity germanium detector
Heritage-based GRS
A flight spare, engineering model,
or repeat of the Psyche design
Previous Missions: MEGANE·MESSENGER·Psyche one agency contributing a gamma-ray spectrometer to another agency's small-body mission.
WHAT’S NEXT?
01
Leadership approval
Authorise engagement on a payload contribution.
02
ESA / JAXA accommodation discussion
Confirm the route and the mission-of-opportunity mechanism.
03
APL / LLNL technical engagement
Open the first technical exchange.
Accommodation detail, open technical items and export-control considerations in appendix.
13
Public عام

## Slide 15
BASELINE KNOWLEDGE GAPS SELECTION RECOMMENDATION VALUE
Why This Matters to SSA
01
Scientific
Adds a dataset RAMSES cannot generate independently.
02
Strategic
Moves SSA from observer to contributor on a flagship mission.
03
Programmatic
Uses a proven instrument and a proven partnership model.
04
Actionable
A credible acquisition route exists now.
Public عام

## Slide 16
Thank you!
Public عام

## Slide 17
APPENDIX
Candidate Trade Study — Full Assessment
Architecture is a screening criterion, not a differentiator. A candidate is scored only until the criterion that removes it.
Candidate | Architecture | Scientific complementarity | TRL | Operational complexity | Power
Gamma-Ray Spectrometer | Fits orbiter | Complements | High | Low | Modest
Neutron Spectrometer | Fits orbiter | Partial | High | Low | Modest
Mössbauer Spectrometer | Requires lander | — | High | — | —
MicrOmega Microscope | Requires lander | — | High | — | —
LIBS, ChemCam class | Requires close range | — | High | — | —
Incompatible with an orbiter-only contribution
Mössbauer and MicrOmega are contact instruments requiring a landed platform; LIBS is close-range and requires high pointing precision. Establishing that sub-surface observation does not require a landing removed the premise beneath all three.
Separated on scientific complementarity
Neutron spectroscopy primarily constrains hydrogen and volatile abundance, which does not enter the mineralogical inversion. Resolving this gap requires multi-element ratios such as Mg/Si and Fe/Si.
The wrong quantity, well accessed
LIBS solves access better than any other candidate and still returns the wrong quantity. Bulk elemental abundance barely moves under weathering, so profiling elements through the rind would most likely return no difference.
Public عام

## Slide 18
APPENDIX
Accommodation & Open Technical Items
Detail supporting the recommendation and the first technical exchange.
Platform: main orbiter, not Farinella
The cooled germanium sensor exceeds what a 6U-XL CubeSat carries in mass and standing power, and the measurement needs an accumulation window of months. It also belongs beside HAMLET: a shared platform means shared observation geometry and coverage, which is what permits one map to be subtracted from the other.
Spatial resolution
Reads a broad patch, tens to hundreds of metres. The mission already maps in detail; this supplies the calibrated value that map is read against.
Integration time
Gamma emission is faint, so precision accumulates over hours and days. The instrument is passive — no laser, no mechanism, no pointing — and gathers while the spacecraft works.
PARTNERSHIP — GAMMA-RAY SPECTROMETERS BUILT
Laboratory | Role | Instruments built
Johns Hopkins APL | Instrument lead and integrator | NEAR Shoemaker, MESSENGER, MEGANE, Psyche, Dragonfly
Lawrence Livermore NL | High-purity germanium sensor | MESSENGER, MEGANE, Psyche
OPEN FOR THE FIRST TECHNICAL EXCHANGE
Footprint achievable at the planned operating altitude.
Boom against body mounting — spacecraft materials generate the same background the instrument measures.
Export control and technology transfer: both laboratories are United States national laboratories.
Public عام

## Slide 19
APPENDIX
Knowledge Gap Register — Evidence
Why no confirmed instrument meets each registered gap.
ID | Knowledge gap | Why no confirmed instrument meets it | Outcome
GAP-1 | Hydration state | HAMLET's range ends at 1500 nm. The diagnostic OH and water bands near 2.0 and 3.0 µm fall outside it, and no other instrument covers that region. | Removed — scientific value
GAP-2 | Weathering-corrected composition | All compositional instruments observe only the space-weathered surface layer. No independent reference exists against which the correction can be established. | SELECTED
GAP-3 | Regolith grain-size distribution | TIRI already bears on grain size through thermal inertia. It is a proxy rather than a direct measurement, but it is one the mission already returns, and measuring the distribution itself needs surface contact an orbiter payload cannot give. | Removed — mission compatibility
GAP-4 | Free Fe–Ni metallic phase fraction | MARIE and HAMLET each give indirect indications of metal content, but neither separates free metallic iron from iron bound in silicates or oxides. | Removed — scientific value
HOW THE CONFIRMED PAYLOAD BEARS ON EACH GAP
HAMLET
Closed inference, maturity map derived from the spectrum it would correct
TIRI
Supplies grain size already, so this study need not measure it
Radar
Unrelated, dielectric measurement is blind to nanophase iron
CHANCES / AFC
No overlap, locates where fresh material may be, never quantifies it
Public عام