## Slide 1
SSA SUMMER TRAINING | JULY - AUGUST 2026
Noora AlQuaydhib Summer Training Journey
Scientific Gap Assessment and Payload Recommendation for RAMSES Mission for Asteroid (99942) Apophis
Supervised by Najla AlAhmadi & Rawan AlRayes
Public عام

## Slide 2
Context & Strategic Rationale
01
The Event
On 13 April 2029. Apophis passes within ~32,000 km, closer than geostationary satellites, visible to the naked eye.
02
The Mission
ESA has committed. ~EUR 150 million with OHB Italia. Now in build. Launch spring 2028, arrival February 2029.
03
The Platform
A spacecraft in build still accepts payload conversations. The encounter will not recur.
04
The Goal
An SSA instrument converts observer status into participant status on a joint ESA–JAXA mission.
The question is no longer whether to participate.
Phase 1 settled the mission. What remains is to put a specific, technically credible contribution on the table while the build phase can still accommodate it.
1
Public عام

## Slide 3
Study Objective & Scope
The second phase of a two-part programme. The first selected the mission; this one determines the contribution.
WHERE THIS STUDY SITS
PHASE 1 — COMPLETED
Asteroid Mission Study
11 missions benchmarked → 2 prioritized → RAMSES selected.
PHASE 2 — THIS STUDY
Payload Study
What does SSA put on the mission?
OBJECTIVE
Identify the single measurement opportunity where an additional national payload would most increase the scientific return of RAMSES and carry it to a named instrument and a named route to obtaining it.
SCOPE BOUNDARIES
Confirmed payload by ESA only.
Must fit the existing architecture: no new spacecraft, stage or surface asset.
Methodology self-contained; heritage missions are context, not evidence.
2
Public عام

## Slide 4
RAMSES Mission Overview
Rapid Apophis Mission for Space Safety , joint ESA–JAXA planetary defence mission.
TARGET & TIMELINE
Designation
Asteroid (99942) Apophis
Size
~375 m across
Taxonomy
Sq type, LL chondrite analogue
Launch
Spring 2028, H3 Rocket, Tanegashima
Arrival
February 2029
Close flyby
13 April 2029, ~32,000 km
MISSION PUBLISHED OBJECTIVES
O1
Shape, orbit and rotation
Before-and-after survey of shape, surface, orbit, rotation and orientation.
O2
Composition and interior
Composition, interior structure, cohesion, mass, density and porosity.
O3
Tidal response
How the asteroid responds to Earth's tidal forces.
O4
Solar System science
Insight into the formation and evolution of the Solar System.
Payload architecture: three platforms, twelve confirmed instruments
Main Orbiter
6 INSTRUMENTS
AFC (×2) · CHANCES · HAMLET · TIRI · RSE · RPS
Farinella: orbiter CubeSat
3 INSTRUMENTS
HORUS · Low-frequency radar · VISTA
Don Quijote: lander CubeSat
3 INSTRUMENTS
SIA · Gravimeter · MARIE
3
Public عام

## Slide 5
Analysis Methodology
A structured analysis narrowed the opportunity to one payload
RAMSES baseline
Studied the mission objectives, platforms and payloads
Mission Measurements
Analysed the measurements against objectives, then constructed them through a framework of multi-variables
Knowledge gaps
Determined knowledge gaps by extracting the non measured measurements
Payload trade study
Searched for a set of compatible payloads
One recommended payload
4
Public عام

## Slide 6
What RAMSES Already Measures
Confirmed payload by platform
Main Orbiter
AFC (×2)
Wide-field imaging, shape
CHANCES
Colour imaging, change detection
HAMLET
Hyperspectral, 650–1500 nm
TIRI
Thermal infrared, grain size
RSE
Radio science, gravity, tides
RPS
Charged-particle environment
Farinella · Orbiter CubeSat
HORUS
Close-range imaging
Radar
Interior structure, metre scale
VISTA
Dust volatiles and organics
Don Quijote · Lander CubeSat
SIA
Surface seismometry
Gravimeter
Local density distribution
MARIE
Surface magnetometry
5
Public عام
BASELINE OPPORTUNITIES SELECTION RECOMMENDATION VALUE

## Slide 7
BASELINE OPPORTUNITIES SELECTION RECOMMENDATION VALUE
Four Scientific Opportunities
Measurement openings the mission never set out to address, registered only where no confirmed instrument meets them.
GAP-1
Hydration state
GAP-2
GAP-3
Regolith grain-size distribution
GAP-4
Free Fe–Ni metallic phase fraction
Weathering-corrected composition was the only opportunity that was both scientifically differentiated and complementary to the existing payload.
6
Public عام
Weathering-corrected composition

## Slide 8
BASELINE OPPORTUNITIES SELECTION RECOMMENDATION VALUE
Priority Selection
Four opportunities passed through three lenses in fixed order, plus an overlap test against the existing requirement set.
Four identified knowledge gaps
GAP-1
GAP-2
GAP-3
GAP-4
1
Strategic fit
Unique to the 2029 encounter and compatible with the architecture
GAP-4, GAP-1 out
2
Scientific value
Not an answer already known before the mission flies
Both confirmed out
3
Mission compatibility
Not already addressed by the existing requirement set
GAP-3 out
ONE PRIORITY
Weathering-corrected composition
Touched by no requirement and
by no confirmed instrument.
7
Public عام

## Slide 9
BASELINE OPPORTUNITIES SELECTION RECOMMENDATION VALUE
The Scientific Problem
Space weathering changes what we see without changing the bulk composition.
Fresh material
Space weathering
Altered optical spectrum
Biased mineralogical interpretation
RAMSES can measure the spectrum.
BUT it cannot independently measure the reference needed to correct it.
The correction closes on itself
HAMLET's maturity map is derived from the spectrum it would correct, which makes it verifiable only against its source
Why it matters at Apophis
Sq type: a surface partly but not wholly refreshed. The 2029 encounter may reset the maturity clock, a natural experiment that will not recur.
8
Public عام

## Slide 10
BASELINE OPPORTUNITIES SELECTION RECOMMENDATION VALUE
The Required Observable
What measurement would close the opportunity?
Independent elemental abundance
of the near-surface regolith
1
From orbit
The correction is applied to maps. A reference from a single landing site cannot travel across a body.
2
Below the weathered surface
Sampling depth must exceed the altered layer, or the reference carries the bias it was meant to remove.
3
Independent of reflected light
A route through the spectrum would inherit the bias it exists to correct.
This defines the instrument requirement before any instrument is selected.
9
Public عام

## Slide 11
BASELINE OPPORTUNITIES SELECTION RECOMMENDATION VALUE
Candidate Payload Assessment
Five candidate payloads were assessed against the required observable and the orbiter, only architecture.
Mössbauer Spectrometer
✕
Landing required
MicrOmega Microscope
✕
Landing required
LIBS, ChemCam class
✕
Close-range operation required
Neutron Spectrometer
!
Partial scientific match
Gamma-Ray Spectrometer
✓
Direct match
GRS is the only candidate that directly measures the required observable from the existing mission architecture.
Full five-criteria assessment in appendix.
10
Public عام

## Slide 12
BASELINE OPPORTUNITIES SELECTION RECOMMENDATION VALUE
Recommendation
RECOMMENDED PAYLOAD ENHANCEMENT
Gamma-Ray Spectrometer
RAMSES Main Orbiter
WHY
01
Independent of reflected light
02
Measures elemental abundance
03
Samples below the weathered layer
04
Strengthens HAMLET's interpretation
05
Fits the existing mission architecture
HAMLET
Mineralogy
+
GRS
Elements
More effecient
composition
11
Public عام

## Slide 13
BASELINE OPPORTUNITIES SELECTION RECOMMENDATION VALUE
Implementation Route
A proven implementation route exists
APL
Johns Hopkins Applied Physics Laboratory
Instrument lead & integration
LLNL
Lawrence Livermore National Laboratory
High-purity germanium detector
Heritage-based GRS
A flight spare, engineering model,
or repeat of the Psyche design
Precedent: MEGANE · MESSENGER · Psyche one agency contributing a gamma-ray spectrometer to another agency's small-body mission.
WHAT’S NEXT?
01
Leadership approval
Authorise engagement on a payload contribution.
02
ESA / JAXA accommodation discussion
Confirm the route and the mission-of-opportunity mechanism.
03
APL / LLNL technical engagement
Open the first technical exchange.
Accommodation detail, open technical items and export-control considerations in appendix.
12
Public عام

## Slide 14
BASELINE OPPORTUNITIES SELECTION RECOMMENDATION VALUE
Why This Matters to SSA
01
Scientific
Adds a dataset RAMSES cannot generate independently.
02
Strategic
Moves SSA from observer to contributor on a flagship mission.
03
Programmatic
Uses a proven instrument and a proven partnership model.
04
Actionable
A credible acquisition route exists now.
Public عام

## Slide 15
Thank you!
Public عام

## Slide 16
APPENDIX
Candidate Trade Study — Full Assessment
Architecture is a screening criterion, not a differentiator. A candidate is scored only until the criterion that removes it.
Candidate | Architecture | Scientific complementarity | TRL | Operational complexity | Power
Gamma-Ray Spectrometer | Fits orbiter | Complements | High | Low | Modest
Neutron Spectrometer | Fits orbiter | Partial | High | Low | Modest
Mössbauer Spectrometer | Requires lander | — | High | — | —
MicrOmega Microscope | Requires lander | — | High | — | —
LIBS, ChemCam class | Requires close range | — | High | — | —
Incompatible with an orbiter-only contribution
Mössbauer and MicrOmega are contact instruments requiring a landed platform; LIBS is close-range and requires high pointing precision. Establishing that sub-surface observation does not require a landing removed the premise beneath all three.
Separated on scientific complementarity
Neutron spectroscopy primarily constrains hydrogen and volatile abundance, which does not enter the mineralogical inversion. Resolving this gap requires multi-element ratios such as Mg/Si and Fe/Si.
The wrong quantity, well accessed
LIBS solves access better than any other candidate and still returns the wrong quantity. Bulk elemental abundance barely moves under weathering, so profiling elements through the rind would most likely return no difference.
Public عام

## Slide 17
APPENDIX
Accommodation & Open Technical Items
Detail supporting the recommendation and the first technical exchange.
Platform: main orbiter, not Farinella
The cooled germanium sensor exceeds what a 6U-XL CubeSat carries in mass and standing power, and the measurement needs an accumulation window of months. It also belongs beside HAMLET: a shared platform means shared observation geometry and coverage, which is what permits one map to be subtracted from the other.
Spatial resolution
Reads a broad patch, tens to hundreds of metres. The mission already maps in detail; this supplies the calibrated value that map is read against.
Integration time
Gamma emission is faint, so precision accumulates over hours and days. The instrument is passive — no laser, no mechanism, no pointing — and gathers while the spacecraft works.
PARTNERSHIP — GAMMA-RAY SPECTROMETERS BUILT
Laboratory | Role | Instruments built
Johns Hopkins APL | Instrument lead and integrator | NEAR Shoemaker, MESSENGER, MEGANE, Psyche, Dragonfly
Lawrence Livermore NL | High-purity germanium sensor | MESSENGER, MEGANE, Psyche
OPEN FOR THE FIRST TECHNICAL EXCHANGE
Footprint achievable at the planned operating altitude.
Boom against body mounting — spacecraft materials generate the same background the instrument measures.
Export control and technology transfer: both laboratories are United States national laboratories.
Public عام

## Slide 18
APPENDIX
Opportunity Register — Evidence
Why no confirmed instrument meets each registered opportunity.
ID | Opportunity | Why no confirmed instrument meets it | Outcome
GAP-1 | Hydration state | HAMLET's range ends at 1500 nm. The diagnostic OH and water bands near 2.0 and 3.0 µm fall outside it, and no other instrument covers that region. | Removed — strategist / scientist
GAP-2 | Weathering-corrected composition | All compositional instruments observe only the space-weathered surface layer. No independent reference exists against which the correction can be established. | SELECTED
GAP-3 | Regolith grain-size distribution | Only TIRI bears on grain size, through thermal inertia, which is a proxy. Under the study's proxy rule a proxy does not close a requirement. | Removed — overlap test
GAP-4 | Free Fe–Ni metallic phase fraction | MARIE and HAMLET each give indirect indications of metal content, but neither separates free metallic iron from iron bound in silicates or oxides. | Removed — strategist / scientist
OVERLAP CHECK AGAINST THE CONFIRMED PAYLOAD
HAMLET
Closed inference, maturity map derived from the spectrum it would correct
TIRI
Useful, supplies grain size, so this study need not measure it
Radar
Unrelated, dielectric measurement is blind to nanophase iron
CHANCES / AFC
No overlap, locates where fresh material may be, never quantifies it
Public عام